## Slide 1: PhD Image Holder
Trying to consolidate and structure everything under one location

## Slide 2
SUMO Drivers
Characteristics / Rules of behavior
Type
LOS Expectations
Consume/Use
Infrastructure Asset
Physical Attributes
Environmental Attributes
Deterioration Rate
Risk (Consequence)
Performance
(Actual LOS)
Condition Rating
Infrastructure Owners
Objectives
Budget
Organizational Constraints
Risk Tolerance
Action Trigger Policy
Maintenance Activity
TAMP Activity Schedule
Route Choice
Threshold
(Priority)
Level of Satisfaction
Legend
ACTION
Static Parameter
Time Dependent Parameter
Action & Time Dependent Parameter
PhD Research - Agents and Roadway (environment) Dynamics
Agent
Environment
Agent
Emergency Alert
modifies
Modified version from

## Slide 3
SUMO Drivers
Characteristics / Rules of behavior
Type
LOS Expectations
Consume/Use
Infrastructure Asset
Physical Attributes
Environmental Attributes
Deterioration Rate
Risk (Consequence)
Performance
(Actual LOS)
Condition Rating
Infrastructure Owners
Objectives
Budget
Organizational Constraints
Risk Tolerance
Action Trigger Policy
Maintenance Activity
TAMP Activity Schedule
Route Choice
Threshold
(Priority)
Level of Satisfaction
Legend
ACTION
Static Parameter
Time Dependent Parameter
Action & Time Dependent Parameter
PhD Research - Agents and Roadway (environment) Dynamics
Agent
Environment
Agent
Emergency Alert
modifies
Modified version from

## Slide 4
SUMO Drivers
Characteristics / Rules of behavior
Type
LOS Expectations
Consume/Use
Infrastructure Asset
Physical Attributes
Environmental Attributes
Deterioration Rate
Risk (Consequence)
Performance
(Actual LOS)
Condition Rating
Infrastructure Owners
Objectives
Budget
Organizational Constraints
Risk Tolerance
Action Trigger Policy
Maintenance Activity
TAMP Activity Schedule
Route Choice
Threshold
(Priority)
Level of Satisfaction
Legend
ACTION
Static Parameter
Time Dependent Parameter
Action & Time Dependent Parameter
Network Demand
Virtual Network
Agent
Emergency Alert
modifies
Relationship Visualization concept from:
H. Osman / Automation in Construction 28 (2012) 45-57

## Slide 6
Vehicle type distribution
Network Demand
Description_of_Network_Demand
Users
Routes
veh per hour
types
etc…
Calibrators
Data sources
Specific roadway flow counts
Routes
Heuristics
Try without and see if we can go for a longer
Dynamic User Assignment
Users Behavior
Introduction leads to Why this Model is Relevant?
Problem Statement
Why this model helps at all?
Questions to be answered
Background and Literature Review
Very relevant papers or projects
Literature Review
Papers By Topic
ABM and Hybrid Models
Etc..
Transportation Asset Management
Hybrid ABM of Infrastructure AM
Infrastructure Asset Own Agent
Description of Owner Agent Purpose Capabilities
Operation Research Scheduling Decision Module
Description of how the schedule will be made inputs outputs
Scenarios to run
Objective Function
Constraints
metrics
Virtual Network Modification Module Python Code
Description of how O agent interacts with V network
True to constraints of OR Schedule
Physical Representation of workforce enforces logic controls
Work crews like buses with special stops
TRAci Python SUMO Interface
Link back to network parameters
O agent collects simulation network run data for OR module
Frequency and Accuracy of update based on agent characteristics
Virtual Network
Description of virtual network
Why SUMO
Components
Physical layout – OSM
Roadway parameterization
Names; lane width, max speed; permissions; etc…
Show Dataframe
O agent HQ locations
Introduction and Background Info

## Slide 7: Vehicle Types
Units:
  Speed = m/s
  Length = m

## Slide 8: Traffic Count Data -Bad Data Format
West Bound
East Bound
114: Files
file:///C:\Users\Biko\Dropbox\PhD\Research\Models\SUMO\DVRPC\Traffic%20Counts\33rd%20and%20Market%20Counts.xlsx
file:///C:\Users\Biko\Dropbox\PhD\Research\Models\SUMO\DVRPC\Traffic%20Counts\Counts%20OSM%202%20-%20V-2\DVRPC%20Traffic%20Counts%20For%20Net%20OSM%202%20-%20V-2_D.xlsm

## Slide 9: DVRPC – Manual Class Distribution
file:///C:\Users\Biko\Dropbox\PhD\Research\Models\SUMO\DVRPC\Traffic%20Counts\PennDOT%20Traffic%20Class%20Distributions.xlsm
http://www.dvrpc.org/webmaps/TrafficCounts/ - Output is only PDF.

## Slide 10: West Philadelphia SUMO Model – 8.23.17
Maybe

## Slide 11: The SUMO Simulation
3
Population Generation and Activity Plan - Fixed
DVRPC House Hold Survey Data Generated Trips
DVRPC Traffic Flow Detector Data Generated Trips
Routing Algorithm:
Minimization of travel time.
  Max speed on a road is based on density and condition
SUMO - Simulation
Asset Information
Asset Profile; including-> Max Speed(condition/Capacity)
Car Following Model Parameters - Fixed
External Database
Potential Outputs:
  queue-output - Save the vehicle queues at the junctions (experimental)
  summary-output - Save aggregated vehicle departure info
  tripinfo-output - Save single vehicle trip info
  vehroute-output - Save single vehicle route info into
    exit-times - Write the exit times for all edges
    Sorted - Sorts the output by departure time
    intended-depart - Write the output with the intended instead of the real departure time
    route-length - Include total route length in the output;
  lanechange-output - Record lane changes and their motivations for all vehicles
  Link-output - Save links states
---Wiki-LINK---
Notes: http://sumo.dlr.de/wiki/Simulation/Output

## Slide 12: Development of AOI
  Area of interest (AOI) within SUMO has been established to include Powelton Village, University City, and segments of other neighborhoods just across the Schuylkill River.
    SUMO’s network topology was created with the assistance of Open Street Maps (OSM),
      An open source mapping database that maintains data on roads, public transit, trails, points of interest, and many more. The critical information that is contained within the database, for this project is the details for each roadway segment.
      Included in the SUMO platform is a tool to directly can import most of the OSM data to construct a functional SUMO network.
https://www.openstreetmap.org/export#map=15/39.9557/-75.1832
SUMO - Network File

## Slide 13: SUMO Simulation - General Flow
Network
Junctions
  Stop sign or Traffic Light or Priority Stop
Edges
  Lane
    Width, Permission, Max Speed, Network Link Type
Additional Properties
  Calibrator
    Triggered Object
      Adds or Removes per defined Vehicles per hour
        DVRPC – Volume Data
OutPuts: ---LINK---
  queue-output
  summary-output
  tripinfo-output
  vehroute-output
    exit-times
    sorted
    intended-depart
    route-length
  lanechange-output
Demand
DVRPC HH Survey Trip Demand with Calibrators
  Vehicle Type distribution – DVRPC Class Data
  Vehicle ID; Vehicle Type; Individual Vehicle Routes; Departure period
Simulation - .SUMOcnfg
Input:
  Network File
  Route File
  vType File
    Calibrator definitions
  Shape Files – for Buildings and Places of interest
1
2
3
4

## Slide 14: DVRPC Data Incorporated Into Sumo’s Traffic Demand
  DVRPC Traffic Count and Manual (vehicle) Class has been incorporated into SUMO as traffic demand and vehicle type distributions
    Each traffic count data set is translated into SUMO be creating a route probe and corresponding calibrator
      95% - completed, but now the process is semi-automated and completion is expected by the 18th of September
      SUMO –Route Probe and Calibrator File
      Vehicle type distribution – from 14 Manual Class Data Points
Incorporated the DVRPC House Hold Trip Survey Data that either originated or ended within the AOI (97%)
  Used Python Gmap Module to generate directions for trips into, out of, and within the AIO (1700+)  Map the turn-by-turn GPS coordinates from Google Directions with GIS  Use GIS to associate routes that entered or exited the AOI with the corresponding perimeter TAZ  Modified the DVRPC trips to their new origin or destination TAZ within the AOI  Create a SUMO Trip file with original departure times  Generate vehicles and routes for each trip
DVRPC Traffic Count Data
Notes: https://www.dropbox.com/s/h7y28db3f12calv/DVRPC Traffic Counts For Net OSM 2 - V-3 9.1.xlsb.xlsx?dl=0
https://www.dropbox.com/s/709opumzrtlf6ys/GIS_TAZ_to_TAZ_All.png?dl=0

## Slide 15: DVRPC – Data and Methods to Incorporate into SUMO

## Slide 16: DVRPC – House Hold Trip Surveys
Household travel surveys are used to obtain information about work and non-work trip generation, trip distribution, modal split, and average vehicle occupancy. Updated household travel information can be used for modeling purposes as well as transportation planning projects such as high occupancy vehicle lanes, bicycle, and pedestrian studies, welfare-to-work programs, and traffic control studies.
Each trip contains an origin and destination Traffic Analysis Zone (TAZ), more on the next slide.
http://www.dvrpc.org/Transportation/Modeling/Data/

## Slide 17: Incorporating DVRPC HH Trip Survey Data into SUMO
There are 3,158 TAZs located within DVRPC’s jurisdiction
The AOI for this project contains ~50 TAZs (some changes to the SUMO TAZ definitions need to be made for more robust routing results)
To utilize the DVRPC’s trip data the trips containing any of the TAZs within the AOI need to be extracted.
Some of the TAZs will fall outside the AOI and need to be mapped to their entry or exit TAZ.
  The Lat and Long coordinates of each TAZs’ centroid are identified with GIS.
  Each trip is associated with the coordinates of its Origin and Destination
  Each trip is sent to Google Maps utilizing Python-Gmap Module.
  The turn by turn results are processed and sent back to GIS
  Each trip’s route is then associated with an AOI edge TAZ
  The original trips are then modified to include their corresponding edge AOI
The modified trips definitions are formatted into a SUMO useable code:
  <trip id="65309" depart="0" fromTaz="TAZ-1032” toTaz="TAZ-1038"/>
  Where the trip id corresponds to the DVRPC HH survey and reported departure time
Notes: C:\Sumo\runs\West_Philly\OSM_Clipped_Vtype_Routes\OSM_Clipped_TAZ_FULLish.trip.xml

## Slide 18: Defining TAZs in SUMO
Defined in SUMO as:
<taz id="TAZ_ID>" edges=“<Road_ID> <Road_ID> .../>
TAZ polygons are imported from GIS into the SUMO network.
The roads are carefully selected within each polygon, incorporating any roads on the northern and eastern edges.
The selected roads are then saved as TAZ-####
Some TAZs have limited roadways, which causes trouble during the routing phase.
  These smaller TAZs are combined with their neighbors
  Combining TAZs should be done in conjunction with the GIS TAZ mapping phase

## Slide 19: Mapping TAZs- From outside the AOI to the edges
Notes: file:///C:\Users\Biko\Dropbox\PhD\Research\Models\SUMO\DVRPC\TAZ\Traffic_Count_TAZ_SpatialJoin_1.xlsx

## Slide 20: Accidents Happen…
--ignore-accidents <BOOL> | Do not check whether accidents occur; default: false
--collision.action <STRING> | How to deal with collisions: [none,warn,teleport,remove]; default: teleport
--collision.stoptime <TIME> | Let vehicle stop for TIME before performing collision.action (except for action 'none')
--collision.check-junctions <BOOL> | Enables collisions checks on junctions; default: false
SUMO Simulation Accident Options

## Slide 21: DVRPC Traffic Models
The following information tries to layout how DVRPC builds and runs their traffic models.

## Slide 22: VISUM – Functionality
Used by Dr. Pradhan’s PhD Student
  “Dongle” is active, but no support is available
Educational / Researcher’s License
  $1,950 – one-time purchase
  2 year – technical support
  Includes Visum, Visim, Viswalk
PTV Visum Functions
Network modelling
Demand calculations
PrT assignment procedures
PuT assignment procedures and operations
Traffic engineering
Create analyses and reports
Interfaces
Notes: Contacted DR. RYERSON (@UPENN) to see if she can use VISUM to generate the TAZ to TAZ O/D Matrix.
-No response yet

## Slide 23: Bridge Division Tasks first pass
Commerce or Fairmount park
Dictates products by funding
Either City, State, or Federally owned
  Mandates requirements and standards to be followed
  If State does not support the City then the City pays 100%
Tasks
Streets Dep.
Highway
Division
Claims and
Lawsuits
Asset Management
PS&E
Drawing Review (other deps)
Bids
Construction
Bridge
Division
Permits
Tech Support
EC&M
Load Rating
Contractors
Information Requests
Contractors -> Chris -> Verify with Owners -> Plans -> Contractor
Inspections
Street’s assets
Other agencies’ assets
Plant inspection
PennDOT inspected
  Special access required
  Special tools required
  Quality Control - audit
Emergency Repairs
Able to work with PennDOT
Emergency repairs needed when:
  Asked by the State, SD/FO, requests for compliance
  Fractural Critical (< 4 stringers)
Oversized vehicles
Overweight vehicles
Sheeting shoring
Crain placement –
citywide
The department of streets are technical (Engineering) experts for most of the City’s other departments for structures
Needs to be updated to reflect TK527
  TK527 is a logging truck. Not very applicable to Philadelphia since the fracking trucks do not come this way, but PennDOT is requiring it
Project and rating primer / refresher
  Pedestrian bridges are rated for emergency services and maintenance vehicles
Plans, Specifications, and Estimates
Electrical Construction & Maintenance (?)

## Slide 24
National
Highway
Trust Fund
Block Grants to States
National Debt
Gas
Tax
General Taxes
Bridges
State Owned
Roads
State Owned
ITS
State Owned
Bridges
Local Owned
Roads
Local Owned
Metro Planning Org
Transit Projects
How Does the Money Flow into State and Local Bridges?

## Slide 25: Life-Cycle Asset Management Activities
5 - Operations And Maintenance – Example of Activities
  Performance Monitoring
  Planned Maintenance
  Service Delivery
  Unplanned Repairs
  Condition Monitoring
  Demand Forecasting
  Deterioration Modelling
  Supply Chain Requirements
6 - Renewal or Disposal - Example of Activities
  Performance Audit
  Improvement And Upgrade
  Replacement
  Closure
  Decommissioning
  Deconstruction, Demolition And Recycling
  Sale
  Transfer Or End Of Liabilities
Civil Infrastructure General Asset Life-Cycle Phases
(Hooper et al. 2009)
Inception
Feasibility Appraisals for Whole-Life Options
Planning and Design
Construction and Handover
Operations and Maintenance
Renewal or Disposal
1
2
3
4
5
6
Asset Management
Damage and Disruptions from Hazards
Deferred Maintenance
Heavy Traffic
Notes: Hooper, R., Armitage, R., Gallagher, A., & Osorio, T. (2009). Whole-life infrastructure asset management: good practice guide for civil infrastructure. Construction Industry Research and Information Association report C, 677.